SAF09-P15

10 June 2009

Laser Safety Policy

_________________________________________________________________________________________

Contents

1.	University Policy

2.	Procedures/guidance

2.1	Responsibilities of the Head of Department

2.2	Appointment of Laser Safety Officers

2.3	Training and competence of Laser Safety Officers

2.4	Duties of Laser Safety Officers

2.5	Responsibilities of Academic Supervisors

2.6	Role of the Laser Safety Advisor

2.7	Laser Safety Technical Group

2.8 	Health, Safety and Environment office

3.	Definitions.

4.	Technical references and further reading

Appendices

Appendix A.	Typical duties of Departmental Laser Safety Officers

Appendix B.	Terms of Reference of the Laser Safety Technical Group

- University policy

To ensure the safety of our staff, students and visitors, it is the policy of Loughborough University to have nominated Departmental Laser Safety Officers in all departments which hold class 3B or class 4 lasers.  The role of the nominated Laser Safety Officer is to co-ordinate the safe use of lasers within the Department.

The University sees the appointment of competent Departmental Laser Safety Officers as vital in ensuring the health and safety of staff, students and visitors and in enabling the University to discharge it’s statutory duties.

The main legislation which is relevant to this subject is the Health and Safety at Work etc Act 1974, the Management of Health and Safety at Work Regulations 1999, and the Provision and Use of Work Equipment Regulations 1998.

2.	Procedures/guidance

  - Responsibilities of the Head of Department

It is a formal requirement of the University that all Departments have designated Laser Safety Officers.  It is the responsibility of the Head of Department to appoint an appropriate person in this capacity. It is recommended that the Departmental Safety Officer should be consulted on this appointment. Guidance on the competency of a Laser Safety Officer is given in Section 2.3.

Implementation of the University Laser Safety Policy within a particular Department lies with the Head of Department. The Head of Department should be satisfied that all relevant staff within their area of responsibility are aware of this policy.

  - Appointment of Laser Safety Officers

When appointing persons as Laser Safety Officers, serious consideration should be given to the amount of time necessary to adequately carry out the associated duties and the persons existing duties.  Where necessary, some of the persons existing duties may need to be transferred to another person/post.

The Departmental Laser Safety Officer is an advisory and monitoring role. The responsibility for ensuring that information provided is incorporated into risk assessment, that risk assessments are carried out and complied with rests with the Academic Supervisor (see Section 2.5).

Persons appointed to the role of Laser Safety Officers should be sufficiently competent through experience and/or qualification to carry out the role. Alternatively they should be willing to undertake training (when necessary) to an acceptable level of competence.  They should also be of sufficient seniority and experience to be able to carry out their duties in relation to laser safety with the recognised authority of the Head of Department.

Heads of Department shall ensure that the University Health and Safety Officer is kept informed of the current nominated Laser Safety Officer for their department.

A full list of Departmental Laser Safety Officers and their contact details are available at; http://www.lboro.ac.uk/admin/hse/contacts/index.html

  - Training and competence of Laser Safety Officers

Departmental Laser Safety Officers shall, as a minimum standard, have undertaken the University two day laser safety training course, or hold a formal qualification demonstrating competency in the safety and use of class 3B lasers or above.

The appointment of a Laser Safety Officer shall be considered as probationary by the University, until they have completed the basic University two day laser safety course (or the similar National Radiation Protection Board (NRPB) laser safety course).

2.4	Duties of Laser Safety Officers

The primary role/duty of Laser Safety Officers is to ensure the safe use of lasers throughout their designated Department, on behalf of the Head of Department. The Laser Safety Officer will ensure lasers are used in line with sector safety guidance and relevant British Standards. (see “Technical references and further reading”). They will act as a source of advice on laser safety to staff and students whose work involves the use of laser equipment. They will liaise between the Department and the University Health, Safety and Environment office on laser safety issues.

The specific duties of Laser Safety Officers shall be determined by the Head of Department, to suit the particular needs of the area.  These shall be clearly documented and formally accepted by the nominated Laser Safety Officer. Typical duties of a Laser Safety Officer are shown in Appendix A.

2.5	Responsibilities of Academic Supervisors

Academic supervisors carry personal responsibility for carrying out risk assessments whenever using lasers as part of their teaching or research duties.

It is the responsibility of individual academic supervisors to provide adequate supervision of their students (both postgraduate and undergraduate) to ensure they are working in a manner which is compliant with the risk assessment.

Responsibility for complying with the Laser Safety Policy rests initially with the Academic Supervisor and ultimately with the Head of Department.

2.6	Role of the Laser Safety Advisor

To ensure there is a source of professional, impartial advice on laser safety, 		the University Health and Safety Officer will appoint a Laser Safety Advisor.

The Laser Safety Advisor will provide advice to the University Health Safety & 		Environment office and to Laser Safety Officers on request.

The Laser Safety Advisor will undertake inspections of laser installations and 		advise on laser operation, practices and procedures etc. as requested by Laser 		Safety Officers or the Health Safety and Environment office.

The Laser Safety Advisor will provide advice to the Laser Safety Technical 		Group via the group meetings.

Contact details for the University Laser Safety Advisor are available at:- 		http://www.lboro.ac.uk/admin/hse/contacts/index.html

2.7	Laser Safety Technical Group

To ensure consistency in compliance with laser safety requirements and encourage the dissemination of good practice in this field, the University Health and Safety Officer will convene a meeting of the Laser Safety Technical Group on a quarterly basis. For terms of reference for the Laser Safety Technical Group see Appendix B.

2.8	Health, Safety and Environment office

To liaise with, and adequately support the University Laser Safety Advisor, 		Laser Safety Officers and Heads of Department in respect of laser safety 			matters.

To arrange and facilitate quarterly Laser Safety Technical Group 				meetings and to report the minutes and details of the meetings to the 			University Health, Safety and Environment Committee on a regular basis.

Regularly review and amend the University Laser Safety Policy.

To maintain a centrally held register of all high powered lasers (class 3B and 		4) used in Departments. The Health, Safety and Environment office to be 			updated by Laser Safety Officers whenever new lasers are purchased or 			where there are changes in location or changes in existing arrangements, 			which are liable to affect the risk in the use of a laser system.

3.	Definitions

Departmental	A generic title adopted by the University that refers

Laser Safety Officer	to the person within a Department who acts as the main focal point for laser safety matters as detailed in this document.  Post holders will be members of

the Laser Safety Technical Group.

Laser Safety Advisor	A nominated post which has a responsibility to supply technical guidance or information to the Health, Safety and Environment office or to Departmental Laser Safety Officer’s as required. The post-holder will be a member of the Laser Safety Technical Group.

4.	Technical references and further reading

- Safety In Universities: Notes of Guidance, Part 2.1 Lasers, CVCP 1992.

- BS EN 60825-1 2007:- Safety of Laser Products, Equipment classification and requirements.

- BS EN 60825-2 2004 A1 2007:-Safety of Laser Products, Safety of optical fibre communications systems.

- BS EN 60825-4 2006:- Safety of Laser products, Laser guards.

- BS EN 60825-5 2003:- Safety of Laser products, manufacturers checklist for IEC 60825-1.

- BS 60825-8 2006:- Safety of Laser products, guidelines for the safe use of Laser beams on humans.

- BS 60825-12 2004:- Safety of Laser products, safety of free space optical communication systems used for transmission of information.

- BS 60825-13 2006:- Safety of Laser products, measurements for classification of Laser products.

- BS 60825-14 2004:- Safety of Laser products, a users guide.

- The Association of University Radiation Protection Officers (AURPO) Guidance on the safe use of Lasers in education and research (GN 7).

- HS(G) 95; HSE guidance:- “The radiation safety of Lasers used for display purposes”.

APPENDIX A

Typical duties of Departmental Laser Safety Officers

Laser Safety Officers are appointed by Heads of Department to advise and coordinate on matters relating to laser safety. They will:-

- undertake appropriate training to an appropriate level of competence, thus enabling them to discharge their duties;

- be fully familiar with the University’s Laser Safety Policy and assist the Head of Department to develop, implement and periodically review their local rules, procedures and policy;

- be responsible for advising on, or co-ordinating internal laser safety training required by research workers to ensure that adequate safety information, instruction and training is provided to laser users and any other laser area personnel;

- keep an inventory of all high powered lasers (class 3B and 4), used in their Department and update the Health, Safety and Environment office whenever new lasers are purchased or where there are changes in location or changes in existing arrangements, which are liable to affect the risk in the use of a laser system;

- monitor that all laser equipment and processes within their area are maintained in a safe condition and in compliance with appropriate statutory requirements;

- liaise with the Health, Safety and Environment office and the Laser Safety Adviser to establish risk assessment procedures, safe working practices and to ensure compliance with the University Laser Safety Policy;

- oversee/review risk assessments for laser work areas and establish safe working procedures;

- advise Research Supervisors who use lasers, on risk assessments and engineering and administrative controls;

- monitor that safe working practices based on risk assessment are adopted locally, especially for postgraduate work, (in view of the fact that many postgraduate students generally work without direct supervision);

- participate in audits carried out by the Health, Safety and Environment office as necessary;

- attend and contribute to the Departmental Health and Safety Committee;

- refer promptly to the Head of Department or University Health, Safety and Environment office, any health and safety problems which cannot be resolved in a timescale appropriate to the risk;

- act with the delegated authority of the Head of Department in matters of urgency relating to laser safety.

APPENDIX B

Terms of Reference of the Laser Safety Technical Group

Membership of the group shall consist of the Laser Safety Adviser, the University Health and Safety Officer (or nominee), the University Radiation Protection Officer and all Departmental Laser Safety Officer’s.

- The technical group will meet 4 times per academic year.

- The technical group will endeavour to ensure that consistent standards are achieved throughout the University and in particular, that compliance with statutory requirements and relevant Codes of Practice and standards are achieved.

- The technical group will provide a forum for technical discussion on safe working with lasers in line with new or proposed legislation or sector guidance.

- The group will provide a forum for the development of consistent standards of working including safe operational procedures and the development of guidelines for approved schemes of work .

- The group will consider the implications of all incidents and injuries caused by exposure to laser radiations and other aspects of laser use .

- The meetings of the technical group will be minuted and details passed to the Health, Safety and Environment Committee.

- The technical group will also consider progress made and where necessary, report to the Health, Safety & Environment Committee, where it appears that policy changes are required.