Amendment to the Local Rules

Duties of the Radiation Protection Supervisors

(extract from Local Rules, Duties of Appointed Officers, 4.4)

  - The Department Radiation Supervisors will be responsible, in close collaboration with the Radiation Protection Officer, for day-to-day matters of safety and close supervision of radiation work within their own departments. Training will be provided by attendance on suitable professional training courses with refresher training every five years. Their duties will include the following:

- Keeping an up-to-date register of unsealed sources, their use and ultimate  disposal.

- Sending, at intervals of not more than three months, a copy of the current sealed source register or registers and at intervals of not more than 1 month a copy of the unsealed source registers and waste disposal records to the Radiation Protection Officer.

- Carrying out regular checks for contamination where unsealed radioactive materials have been used.

- Carrying out regular leakage surveys on equipment emitting ionising radiations at a frequency of not less than 6 months.

- In consultation with the Radiation Protection Officer, carrying out duties relating to the registration of radiation workers, administration of TLD badges and notification of termination of work together with other general measures controlling safety as laid down in the Local Rules. Exceptionally, in order to ensure the necessary close supervision, it may be necessary to appoint more than one Radiation Protection Supervisor within a Department.

- Ensuring suitable risk assessments are carried out on all new work involving the use of ionising radiation. (see appendix XI)

- Making arrangements for the delivery of appropriate information and training to radiation workers in their area. ( see appendix XII)

- Reporting any suspected loss or theft immediately to the Radiation Protection Officer.

- Reporting any significant accidental exposures, breaches of the local rules or any other matters giving cause for concern to the RPO.

- Keeping a register of all sealed radioactive sources kept permanently in the department together with a record of periodic leakage tests, which must be carried out at regular intervals not exceeding 24 months. Records relating to the whereabouts of each sealed source must be kept up-to-date on  a daily basis.